## Slide 1
Mayank Parasar, Ankit Sinha and Tushar Krishna
Brownian Bubble Router: Enabling Deadlock Freedom via Guaranteed Forward Progress
School of Electrical and Computer Engineering
Georgia Institute of Technology
mparasar3@gatech.edu
ankit.Sinha@gatech.edu
tushar@ece.gatech.edu
http://synergy.ece.gatech.edu

## Slide 2: Many-Core  Networks-on-Chip

## Slide 3: Challenge: Deadlocks
A
D
C
B
Dest. A
Dest.D
Dest. C
Dest. B
Deadlock!

## Slide 4: Challenge: Deadlocks
A
D
C
B
Dest. A
Dest. D
Dest. C
Dest. B
Deadlock!

## Slide 5: Deadlocks: Zoomed-In
A
B
C
D
Dest. D
Dest. A
Dest. B
Dest. C
Deadlock!

## Slide 6: What is a deadlock?
Circular/Cyclic dependency on acquiring buffers leads to deadlock
This renders the forward progress of packets impossible
Correctness problem, can cause complete system failure.
Caused due to cycles in Channel Dependency Graph (CDG)
Depends on both topology and routing algorithm
Notes: Deadlock are caused due to cyclic dependency of buffers
this renders the forward movement of packets
it is a correctness problem as it can let to the failure of whole system; hence needs to be treated as first class citizen.
The fundamental reason for deadlock to occur is because of the cycles in the channel dependency graph
Making channel dependency graph acyclic is tedious process; especially for many core systems
and depends both on topology and routing algorithm

## Slide 7: Outline
Background: Deadlocks
Current Solutions
Brownian Bubble Router
  Concept
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion
Notes: Deadlock is a known problem in networks and significant research efforts has been devoted on making networks deadlock free.
Let us see what are the prior solutions proposed in order to make networks deadlock free

## Slide 8: Current Solutions
Dally’s theory
  Strict order in acquisition of links/buffer
  XY, West-First, Up*/Down*
Duato’s theory
  Acyclic extended CDG
  Escape VC
Flow control based schemes
  Restrict injection to avoid deadlock
  Bubble Flow Control [IPDPS’11]
Deadlock Recovery
  Detect and recover from deadlock
  DISHA [IPDPS’95], Static Bubble [HPCA’17], SPIN [ISCA’18]
Deflection Routing
  Deflect or misroute packets
  BLESS [ISCA’09], CHIPPER [HPCA’11]
Notes: Earlier Solutions proposed can be categorized in following categories:
1. Dally's theory:
make CDG acyclic using routing algorithm, by disallowing certain turns
examples are XY routing, West First routing etc
2. Duato's theory
Allows more path diversity
tries to make the extended CDG to acyclic and proves that as long as there is a path which is acyclic then network is deadlock free
examples are escape VC
3. There are flow control techniques:
which controls the injection of packets in the network such that deadlock cycle never forms.
examples are Bubble Flow Control
4. Deadlock recovery schemes argue that deadlock avoidance allocate excessive hardware just to prevent deadlocks to occur..instead we should detect deadlock and recover from it.
Examples are Disha., static bubble and spin
5. Deflection routing is inherently deadlock free.. however it was originally proposed to reduce the buffer requirement from NOC routers.
examples are BLESS and CHIPPER

## Slide 9: Qualitative Comparison of Deadlock Freedom Mechanisms
Solution Proposed | Full Path Diversity | High Throughput | No Extra VCs | No Deadlock Detection | Topology agnostic
Dally’s Theory |  |  |  |  | 
Duato’s Theory |  |  |  |  | 
Flow Control |  |  |  |  | 
Recovery |  |  |  |  | 
Deflection |  |  |  |  | 
*in all VCs except escape VC
*
Can we do better?
Notes: Let us now Qualitatively categories the proposed solutions in Deadlock on the metric of 'Path diversity' 'high-throughput' 'extra-VCs' 'Deadlock detection' and 'Topology independence'
We see .... <explain each solution>
In general we see there's no solution which fulfills all the desired characteristics which providing deadlock freedom.
Therefore we ask the question: 'Can we do better?'

## Slide 10: Outline
Background: Deadlocks
Current Solutions
Brownian Bubble Router
  Concept
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion
Notes: Now let me introduce to you the concept of BBR and how it takes an orthogonal approach compared to prior work to resolve deadlocks

## Slide 11
A
B
C
D
Dest. D
Dest. A
Dest. B
Dest. C
Deadlock!
C
C
C
C
Empty-VC tagged as ‘Brownian-Bubble’
Free-VC
Enter Brownian Bubble Router
Bubble Movement means reading out packet from its VC and writing it to empty VC marked as ‘Brownian Bubble’
Deadlock
Resolved!
BBR is free from Deadlock-detection complexity!
Notes: This is the same scenario where we see the packets A, B, C and D are involved in deadlock.
Let's see how BBR resolves this deadlock.
BBR guarantees one empty VC per router, tagged as Brownian bubble or simply bubble initialized in each router at the starting of the network.
This bubble randomly moves within the router causing packets to shuffle in the router. Bubble movement simply means reading out packet from the VC where bubble is scheduled to move next and writing the packet back at the current location of the bubble.. effectively moving the bubble at the prior VC of the packet.
Here bubble movement has created the free-VC which was earlier the part of deadlock, ready to be acquired by the packets involved in the deadlock..
this is how BBR resolves the deadlock and now every packet has moved to its destination-router.
One salient point is that unlike deadlock-recovery there's no deadlock-detection is needed in BBR!!

## Slide 12: Nuance about ‘Brownian Bubble’ movement
It moves randomly across input ports at a fixed rate
  In experiments BBR-‘k’, refers to the movement of bubble after ‘k’ cycles
Invariant of Brownian Bubble Router is that there will always be one empty VC at any time in the router
  Initialized randomly at starting of the network
Bubble never goes into the injection-input port of the router
  Otherwise it would get consumed, negating the invariant of Brownian Bubble Router
Notes: Now let us see some of the salient feature of Brownian Bubble
It moves randomly across input port at a fixed rate.. this is a design-time knob we have provided to the network designers and in our experiments we have referred to it as 'BBR-k', which means bubble moves in every k-cycles.
Invariant of BBR is that there will always be one empty VC.. called as bubble or Brownian bubble in the router, this is initialized at the start of the network at randomly chosen input VC except injection input VC
and lastly bubble never goes into the injection input port of the router otherwise it may get consume negating the invariant of BBR

## Slide 13: Deadlock Freedom Proof
As long as there is an unblocked packet present in the router, Brownian Bubble (BB) can effectively replace the deadlocked packet with the unblocked packet
  Unblocked packet: packet requesting non-deadlocked output port
  Corner case if no unblocked packet discussed later
Unblocked packet eventually leaves the router, creating the free VC in the original deadlock ring
Upstream router can then send its earlier deadlocked packet to downstream router, breaking the deadlock ring
Notes: Now let use analyze the proof of deadlock freedom provided by BBR
BBR proposes as long as there's unblocked packet present in the network.. BB can effectively replace the un-blocked packet with the deadlocked packet
we refer Un blocked packet as the one which is requesting non-deadlocked output port
Once unlock packet replaces the original deadlocked packet and leaves the router then it creates a free VC in the router which was originally involved the deadlock ring..
this can be taken up by the upstream router to send the earlier deadlocked packet.. leading to the deadlock resolution

## Slide 14: Outline
Background: Deadlocks
Current Solutions
Brownian Bubble Router
  Concept
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion
Notes: Let's now deep-dive into the micro-architecture and other characteristics of BBR

## Slide 15: BBR Microarchitecture
BBR requires packets from VCs from any port to be able to move to VCs at any other port
BBR bus for bubble movement
Notes: Bubble movement requires packet present in VC of any input port in BBR to be able to move to VC of any other input port in BBR
This requires micro-architectural changes in the router micro-architecture of BBR
Here, we shows the baseline router micro-architecture.. and BBR arguments this micro-architecture by BBR bus which connects all input port except injection input port of the router.
There's credit management unit and bubble movement unit which controls how often to move bubble in the router.

## Slide 16: BBR Microarchitecture
BBR requires packets from VCs from any port to be able to move to VCs at any other port
BBR bus is the appropriate topology for bubble movement within the router
  Only one bubble => no contention!
  Low area overhead: 7.4 %
Can easily be extended to arbitrary number of input ports
  Suitable for high-radix routers and irregular topologies
Notes: We have chosen bus as the topology for movement of bubble because, every BBR contains only one bubble therefore there will not be any contention for acquiring there bus.
as per our evaluation it has low zero overhead: only 7.4%
and BBR bus can be easily extended to arbitrary number of input ports, therefore it is suitable for high-radix routers and irregular topologies

## Slide 17: Brownian Bubble Movement Frequency
Low Bubble Movement Frequency
  Deadlock persists longer  throughput decreases
  Few buffer reads and writes  lesser energy overhead
High Bubble Movement Frequency
  Deadlock resolves faster  throughput increases
  More buffer reads and writes  more energy overhead
    Our optimization: prioritize bubble movement between empty VCs, so that no energy is expended during bubble movement
Notes: Let's now discuss the trade of 'Brownian Bubble Movement Frequency'
We have two choices for bubble movement frequencies in BBR
if we have lower bubble move
...
one of the optimization that we have included in our work is prioritizing bubble movement between empty VCs so that there is no energy expended during bubble movement frequency then deadlock persists longer

## Slide 18: Credit Management
Upstream router is agnostic if the downstream router’s corresponding VC contains bubble or packet.
No Credit sent to upstream router during bubble movement to a non-empty VC
Credit sent to upstream router during bubble movement to an empty VC
Notes: There is need for credit management with the movement of BB in certain cases.
Credit are a way for an upstream router to track the free buffers at downstream router which in turns allow it to send packet to downstream router.
Since upstream router is not allowed to send a packet to a VC where BB is present, it is agnostic if the corresponding downstream router has packet or BB at it's input VC
Consequently, there's no credit exchange when BB exchange places with a packet.
However, if BB exchange place with a empty VC, it needs to send the decrement credit signal to upstream router, informing it that the VC is now occupied.

## Slide 19: Deadlock Freedom Corner Cases
Recall that as long as there is an unblocked packet present in the router, Brownian Bubble (BB) can effectively replace that packet with the one, involved in deadlock
Corner Cases: All packets in router going out of same output port. No amount of bubble movement helps
Notes: Recall that BBR resolves deadlock as long as there's an unblocked packet present in the network by effectively replacing the deadlock packet.. however there could be a cases, as shown below where there is no unblocked packet present in the BBR in those cases bubble movement will not help to resolve the deadlock

## Slide 20: Solution: Bubble Exchange (BE)
Periodically exchange bubble with packets among neighboring routers
  Triggered when an occupancy-threshold is reached
  More details in the paper
Notes: To recovers from those cases, we use the mechanism of 'Bubble Exchange'
The idea is to periodically exchange bubble in router with packets from neighboring router.
based on the occupancy of downstream routers.
Here Occupancy is defined as number of packets sitting in the router compared to total number of input VC available
For more details I would encourage to read the paper.

## Slide 21: Outline
Background: Deadlocks
Current Solutions
Brownian Bubble Router
  Concept
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion
Notes: now let's talk about evaluation methodology used in evaluation of BBR

## Slide 22: Evaluations
Used gem5 and Garnet2.0 for network simulation
BBR uses fully adaptive random routing and hence enjoys full path diversity
BBR evaluated on regular and irregular topologies
Notes: We have used gem5 and Garnet2.0 for our network simulation.
We compared our work with state of art Deadlock Avoidance and Deadlock Recovery schemes
We also evaluated BBR for irregular topologies

## Slide 23: Outline
Background: Deadlocks
Current Solutions
Brownian Bubble Router
  Concept
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion
Notes: Having concept of BBR been illustrated, now's the time for analyzing how BBR performs

## Slide 24: Results: Correctness
All traffic patterns use random routing
How do you detect a deadlock?
  Packets injected = Packets received
  Test for correctness
Network deadlocks early (at low injection rate) when fewer VCs are available
Bit-Complement traffic pattern deadlocks earliest
  has highest cross network traffic

## Slide 25: Result: Performance
Compared against state of art deadlock recovery and deadlock avoidance routing algorithm on 8x8 Mesh
BBR-‘k’ refers the the frequency of Brownian Bubble movement
40% improvement over deadlock avoidance and 2x improvement over deadlock recovery routing algorithm
Notes: These are traditional performance graphs
Explain adaptive routing: whenever there's a choice of router, packet chooses the one which has more free VCs available.
in general we see 40% improvement over state of art deadlock avoidance and 2x improvement overstate of art deadlock recovery schemes.
this is due to the path diversity provided by the Random routing

## Slide 26: Result: Bubble Movement(BM)
At low injection rates there is low probability of deadlocks
There is virtually zero Brownian bubble movement at low injection rate
This is true even for BBR-1, because Bubble Movement gives preference to empty input VC to reduce buffer read and write
Therefore, bubble movement is adaptive in BBR
BBR bubble movement adds negligible buffer reads and writes over baseline
Notes: Now let use see how much is Bubble movement overhead introduced by BBR
Here y-axis shows the %age of bubble movement over buffer reads and writes
At low injection rate there's low probability of deadlocks
and we observer virtually 0 BB movement at low injection rate. ( this normalized to the buffer read and write)
this is because of one of the optimization that we discussed where bubble movement is prioritized for empty VC
therefore BB is adaptive in BBR

## Slide 27: Results: Irregular topology
Traditional turn restriction will no longer work in irregular topology
BBR provides 40% higher throughput over spanning tree routing algorithm
Notes: This slide shows the irregular topology derived from 4x4 Mesh..
here link between node 5 and 6 has been disabled.
rudimentary way of routing packets in irregular topology involves spanning tree construction.
this leads to limited path diversity..
particularly link between router 1 and router 2 will not be used by the spanning tree
BBR on other hand does not incur such complexity...
BBR provides 40% higher throughput over spanning tree because it enjoys more bath diversity

## Slide 28: Outline
Background: Deadlocks
Current Solutions
Brownian Bubble Router
  Concept
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion

## Slide 29: Revisiting Qualitative Comparison
Solution Proposed | Full Path Diversity | High Throughput | No Extra VCs | No Deadlock Detection | Topology agnostic
Dally’s Theory |  |  |  |  | 
Duato’s Theory |  |  |  |  | 
Flow Control |  |  |  |  | 
Recovery |  |  |  |  | 
Deflection |  |  |  |  | 
BBR |  |  |  |  | 
*in all VCs except escape VC
*
Notes: Let's revisit our previous comparison metric where we discuss how previously proposed deadlock freedom schemes performs on the given metric.
We see BBR performs well in all the metric and provides Full path diversity. highthoughput doesn't need extra VC, is topology agnostic and doesn't need to detect deadlock.

## Slide 30: Conclusion
Deadlock is the problem which every network has to deal with
Current solutions either add turn restrictions (sacrificing path diversity), or require additional VCs, or require expensive circuitry to detect and recover from deadlocks
BBR provides a novel way of resolving deadlock by providing one guaranteed empty VC per router (called as ‘Brownian bubble’) that moves at a periodic rate across router’s input port
BBR provides performance benefits over both deadlock avoidance and deadlock recovery schemes at a low area/power overhead
BBR enjoys full path-diversity, requires no additional VCs and is completely topology agnostic
Thank you!
D
C
C
A
BrownianBubble
Router
Questions?