## Slide 1
Mayank Parasar, and Tushar Krishna
BINDU: Deadlock-Freedom with One Bubble in the Network
School of Electrical and Computer Engineering
Georgia Institute of Technology
mparasar3@gatech.edu
tushar@ece.gatech.edu
http://synergy.ece.gatech.edu

## Slide 2: Many-Core  Networks-on-Chip

## Slide 3: Router Micro-Arch
Control
Xbar
Router
West
East
South
North
Core
Buffers
Router micro-architecture

## Slide 4: Challenge: Routing Deadlock
9
5
10
6
5
9
6
10
Deadlock
5
Destination Router-5
Network
Network
Network
Network

## Slide 5: Channel Dependency Graph (CDG)
F
A
B
E
D
C
Function of both Topology and Routing Algorithm
Deadlock occurs because of cycles present in the channel dependency graph of the topology
Cycle

## Slide 6: What is a deadlock?
Renders the forward progress of packets impossible
Correctness problem, can cause complete system failure.
Caused due to cycles in Channel Dependency Graph (CDG)

## Slide 7: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 8: Prior Work
Dally’s theory
  Strict order in acquisition of links/buffer
  XY, West-First, Up*/Down*
Duato’s theory
  Acyclic extended CDG
  Escape VC
Flow Control based schemes
  Restrict injection to avoid deadlock
  Bubble Flow Control [IPDPS’11]
Deadlock Recovery
  Detect and recover from deadlock
  DISHA [IPDPS’95], Static Bubble [HPCA’17], SPIN [ISCA’18]
Deflection Routing
  Deflect or misroute packets
  BLESS [ISCA’09], CHIPPER [HPCA’11]
Forced Movement based schemes
  Periodically shuffle packets in the router
  Brownian Bubble Router [NOCS’18]

## Slide 9: Qualitative Comparison of Deadlock Freedom Mechanisms
Prior Work | Full Path Diversity | High Throughput | No Extra VCs | No Deadlock Detection | Topology agnostic
Dally’s Theory |  |  |  |  | 
Duato’s Theory |  |  |  |  | 
Flow Control |  |  |  |  | 
Recovery |  |  |  |  | 
Deflection |  |  |  |  | 
BBR |  |  |  |  | 
*in all VCs except escape VC
*
Can we do better?

## Slide 10: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 11: BBR: Brownian Bubble Router [NOCS’18]
collision
What if we keep anyone lane always free to begin with?

## Slide 12: BINDU: Bubble in Irregular Network for Deadlock Purging
What if we keep one lane always free in whole road-network to begin with?

## Slide 13: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definitions
  Walk-through
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 14: Definitions
Bindu
Bindu movement
Blocked packet
Unblocked packet
Empty slot

## Slide 15: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 16: BINDU: Walk-through
Bindu Path
Bubble (Bindu)
Bindu Path: Any cyclic path that covers all the input ports of the all the routers in the topology

## Slide 17: BINDU: Walk-through
1
1
2
3
4
4
3
2
C
Deadlock resolved!
Bindu moves in a fixed path visiting all the input ports of the router
It naturally resolves any deadlock that comes in its way by displacing the packets
BINDU is free from Deadlock-detection complexity!
Empty-slot
Deadlock!

## Slide 18: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 19: BINDU: Deadlock Freedom Proof

## Slide 20: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion

## Slide 21: BINDU Router Microarchitecture
Bindu path is confined to VC-0 of each inport (except injection port) of all the routers in the Network

## Slide 22: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 23: Evaluations
Used gem5 and Garnet2.0 for network simulation
In BINDU packet uses fully random minimal routing and hence enjoys full path diversity
BINDU is evaluated on regular and irregular topologies
BINDU is evaluated for both real application and synthetic traffic pattern

## Slide 24: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion

## Slide 25: Results: Synthetic traffic, regular topology
Chart: Injection rate (packets injected/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16
brownian-network(bb-1) | 15.6178 | 15.7889 | 16.1744 | 16.596 | 17.3698 | 18.613 | 84.588 | 114.2694
BBR | 15.9429 | 16.4113 | 17.1044 | 17.9977 | 19.9062 | 484.3102 | 505.0849 | 491.1155
spin | 15.5802 | 15.6723 | 15.928 | 16.1769 | 16.6547 | 17.4278 | 19.5321 | 63.8556
escapeVC | 16.5858 | 18.5811 | 32.041 | 54.9637 | 152.1507
Chart: Injection rate (packets injected/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32
brownian-network(bb-1) | 15.6118 | 15.8047 | 16.0763 | 16.4293 | 17.0127 | 18.1702 | 21.7586 | 154.0622 | 463.0836 | 866.6281 | 773.8445 | 721.554 | 725.9541 | 741.7606 | 756.733 | 766.922
BBR | 15.9217 | 16.3999 | 16.9714 | 17.7934 | 19.4091 | 126.6818 | 877.9103 | 779.7109 | 820.0087 | 837.9207 | 843.0287 | 837.3516 | 826.7579 | 814.2371 | 804.2334 | 798.7732
spin | 15.5943 | 15.7374 | 15.9003 | 16.0904 | 16.4162 | 17.071 | 18.899 | 111.1945 | 602.8044
escapeVC | 16.6419 | 19.0294 | 33.4135 | 187.4757
Chart: Injection rate (packets injected/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32
brownian-network(bb-1) | 13.0849 | 13.2387 | 13.458 | 13.7784 | 14.2343 | 15.1331 | 17.5555 | 746.7826 | 761.8383 | 665.5313 | 713.6699 | 818.6242 | 781.6789 | 806.2212 | 807.5558 | 783.0616
BBR | 13.3406 | 13.7557 | 14.2572 | 14.9848 | 16.1758 | 808.2352 | 860.2459 | 860.3511 | 853.8516 | 836.0419 | 826.3995 | 816.1704 | 806.2634 | 788.2708 | 780.5685 | 775.5471
spin | 13.0686 | 13.1751 | 13.3173 | 13.5057 | 13.8159 | 14.385 | 15.7867 | 71.0477 | 389.6492
escapeVC | 14.2063 | 15.7647 | 24.4017 | 28.759 | 184.4319
Uniform random
Transpose
Shuffle
Fault-0
45% higher throughput over Escape VC
30% higher throughput over BBR
Similar throughput as SPIN without complexities

## Slide 26: Results: Synthetic traffic, irregular topology
Chart: Injection rate (packets injected/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5
brownian-network(bb-1) | 16.125 | 16.3436 | 16.9393 | 18.5002 | 151.9891 | 137.2277 | 170.8003 | 171.7394 | 234.2322 | 141.7114 | 198.1498 | 134.7439 | 281.5996 | 338.5113 | 255.0797 | 205.6798 | 177.1823 | 266.1726 | 282.9411 | 213.4593 | 361.2947 | 149.3555 | 403.514 | 283.0358 | 200.7437
BBR | 16.5115 | 17.2076 | 1072.4141 | 574.2049 | 551.5017 | 557.8318 | 500.4234 | 530.8335 | 480.9401 | 540.3424 | 515.0619 | 500.2764 | 511.2316 | 488.5162 | 439.4677 | 500.1876 | 490.1388 | 449.1593 | 447.0351 | 491.4381 | 477.9425 | 500.4062 | 490.9611 | 482.7915 | 451.6207
spin | 16.1224 | 16.3423 | 16.9629 | 921.1865
escapeVC | 17.7783 | 22.9604 | 87.4285
Chart: Injection rate (packets injected/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5
brownian-network(bb-1) | 15.6556 | 15.9429 | 16.5019 | 18.1436 | 119.7288 | 730.7436 | 622.9135 | 691.8621 | 691.6393 | 743.6767 | 753.5983 | 745.7074 | 752.6736 | 754.6342 | 752.2655 | 752.5886 | 753.4578 | 752.2049 | 748.3922 | 752.5165 | 765.8091 | 775.7737 | 779.6069 | 775.6776 | 763.9606
BBR | 16.097 | 16.9265 | 19.4447 | 666.6029 | 780.4266 | 848.6453 | 864.5907 | 851.0057 | 852.4453 | 839.8192 | 840.3303 | 832.0227 | 820.7106 | 809.526 | 798.86 | 793.599 | 775.5614 | 764.4339 | 755.9008 | 759.6536 | 769.0544 | 775.7907 | 763.8022 | 759.0836 | 750.926
spin | 15.6605 | 15.9504 | 16.4833 | 17.9561 | 87.9349 | 604.3195
escapeVC | 17.601 | 22.5332 | 190.3203
Chart: Injection rate (packets injected/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5
brownian-network(bb-1) | 13.4015 | 13.551 | 13.767 | 14.1656 | 15.4488 | 72.9057 | 984.5787 | 700.7167 | 695.6038 | 707.1666 | 714.7202 | 732.1813 | 738.1981 | 749.4469 | 746.8046 | 745.4442 | 742.3258 | 739.6672 | 743.0445 | 741.2936 | 765.4456 | 772.565 | 779.0206 | 770.819 | 766.0075
BBR | 13.6849 | 14.1333 | 14.8244 | 535.6314 | 807.7312 | 793.319 | 818.2614 | 834.3984 | 852.9355 | 839.6972 | 847.497 | 830.0075 | 821.2095 | 819.422 | 807.795 | 796.3946 | 794.3245 | 777.0665 | 769.8776 | 756.4238 | 753.2679 | 734.5995 | 733.5692 | 719.383 | 706.5465
spin | 13.4017 | 13.5487 | 13.7731 | 14.1965 | 15.5657 | 686.2646
escapeVC | 14.8689 | 17.1915 | 28.274 | 182.0236
Uniform random
Transpose
Shuffle
Fault-12
40% higher throughput over Escape VC
25% higher throughput over Escape VC
10% higher throughput over SPIN

## Slide 27: Results: MOESI Cache Coherence
Chart: Average Packet Latency
| Barnes | Bodytrack | Canneal | FFT | F'animate | FMM | Lu_cb | Lu_ncb | Ocean_cp | Radix | Volrend | Average
Escape VC | 40.4204 | 42.0732 | 46.4428 | 159.5649 | 54.5787 | 42.6343 | 36.7346 | 70.3043 | 247.7772 | 168.3694 | 107.2394 | 92.3763
SPIN | 35.6425 | 35.7729 | 37.1183 | 130.9 | 40.2179 | 37.7313 | 32.5511 | 61.8088 | 138.9135 | 67.7872 | 81.4079 | 63.6229
BBR | 30.2133 | 28.7095 | 35.8195 | 51.4181 | 34.2052 | 32.1975 | 26.7781 | 63.9023 | 63.8974 | 48.886 | 24.629 | 40.0596
BINDU | 28.789 | 26.2834 | 29.7366 | 63.4918 | 30.3601 | 28.612 | 24.9251 | 53.3167 | 53.2956 | 38.2943 | 23.4319 | 36.4124
Chart: Average Packet Latency
| Barnes | Bodytrack | Canneal | FFT | F'animate | FMM | Lu_cb | Lu_ncb | Ocean_cp | Radix | Volrend | Average
Escape VC | 29.4172 | 29.2979 | 29.4994 | 43.6821 | 30.8819 | 32.7665 | 27.9085 | 47.287 | 79.6328 | 37.8885 | 46.4944 | 39.5233
SPIN | 25.9986 | 26.3546 | 25.0486 | 32.7634 | 26.4454 | 29.0533 | 25.3781 | 39.4343 | 46.6958 | 37.8472 | 30.8792 | 31.4453
BBR | 20.716 | 20.0706 | 20.1607 | 25.8411 | 20.8089 | 21.3316 | 19.586 | 31.2417 | 27.854 | 20.6199 | 19.4771 | 22.5189
BINDU | 20.5193 | 20.0377 | 19.7608 | 27.3809 | 20.5299 | 21.0133 | 19.3923 | 31.2666 | 27.9182 | 20.1444 | 19.3035 | 22.4788
Fault-0
Fault-8
out-performs prior deadlock freedom solutions
Higher benefits observed in more fragmented topologies

## Slide 28: Results: MOESI Cache Coherence
Chart: Normalized runtime
| Barnes | Bodytrack | Canneal | FFT | F'animate | FMM | Lu_cb | Lu_ncb | Ocean_cp | Radix | Volrend | Average
Escape VC | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SPIN | 1.0568 | 0.99026 | 0.87397 | 0.8877 | 1.0011 | 0.98867 | 0.98265 | 0.90882 | 1.0393 | 1.1574 | 1.1469 | 1.003
BBR | 0.97339 | 0.98729 | 1.0012 | 0.86531 | 0.99639 | 0.98875 | 0.95969 | 0.8352 | 0.93455 | 1.0121 | 0.99498 | 0.95899
BINDU | 0.96131 | 0.992 | 0.94787 | 0.88265 | 0.97944 | 0.94993 | 0.95642 | 0.80345 | 1.0119 | 0.92493 | 0.99767 | 0.94614
Chart: Normalized runtime
| Barnes | Bodytrack | Canneal | FFT | F'animate | FMM | Lu_cb | Lu_ncb | Ocean_cp | Radix | Volrend | Average
Escape VC | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SPIN | 1.1794 | 0.98459 | 0.9818 | 0.96215 | 1.0001 | 1.0439 | 0.9368 | 0.8957 | 0.82645 | 1.2657 | 0.84597 | 0.99296
BBR | 1.0176 | 0.98638 | 0.93966 | 0.94307 | 0.99193 | 1.0255 | 0.92043 | 0.83387 | 0.64629 | 1.0803 | 0.84272 | 0.92979
BINDU | 1.0129 | 0.98618 | 0.94629 | 0.9383 | 0.99509 | 1.0396 | 0.935 | 0.86881 | 0.68392 | 1.0413 | 0.83925 | 0.93515
Fault-0
Fault-8
7% average reduction in runtime of real applications

## Slide 29: Results: Bindu Sweep
Low-load latency increases with number of Bindus
Low-load latency increases with number of faults
Saturation throughput decreases with number of Bindus
Saturation throughput decreases with number of faults
Effect of Bindu is more pronounced for lower vc-per-input port

## Slide 30: Results: Sensitivity study
Chart: Bindu Movement Period
| 1 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
fault-0 | 0.16 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14
fault-4 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14
fault-8 | 0.1 | 0.12 | 0.1 | 0.12 | 0.1 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12
fault-12 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.08 | 0.08 | 0.08
Chart: Injection rate (packets received/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34
escapeVC | 1.3888 | 1.199 | 1.1271 | 1.0824 | 1.0577 | 1.0457 | 1.0515 | 1.0432 | 1.0556 | 1.0284 | 1.0966 | 1.0839 | 1.0389 | 1.0589 | 1.0563 | 1.053 | 1.0472
SPIN | 1 | 1 | 1 | 1 | 1 | 1 | 2.533 | 2.6438 | 3.8757 | 5.0225 | 3.0948 | 14.103 | 4.1007 | 7.6488 | 3.2921 | 2.8214 | 5.9046
BBR | 1 | 1 | 1 | 1 | 1.1046 | 1.2357 | 1.2612 | 1.2779 | 1.2584 | 1.2786 | 1.3273 | 1.2221 | 1.257 | 1.2387 | 1.2699 | 1.3527 | 1.2044
BINDU-1_1 | 1 | 1.0001 | 1.0002 | 1.0003 | 1.0005 | 1.0008 | 1.1102 | 1.1326 | 1.1349 | 1.1286 | 1.1499 | 1.1284 | 1.1256 | 1.1273 | 1.1254 | 1.1447 | 1.122
BINDU-1_32 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0398 | 1.0649 | 1.1108 | 1.1351 | 1.0738 | 1.1235 | 1.0938 | 1.0948 | 1.0967 | 1.1148 | 1.0837
BINDU-1_64 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0389 | 1.0721 | 1.0803 | 1.0757 | 1.0922 | 1.0799 | 1.0942 | 1.0688 | 1.0987 | 1.0837 | 1.0934
BINDU-1_1_512 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0055 | 1.0106 | 1.0134 | 1.0114 | 1.0117 | 1.0148 | 1.0148 | 1.0209 | 1.0205 | 1.0162 | 1.016
BINDU-1_1024 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0023 | 1.0072 | 1.0071 | 1.0061 | 1.0067 | 1.0057 | 1.0133 | 1.0068 | 1.0197 | 1.007 | 1.0078
Saturation throughput decreases with increase in Bindu Movement Period
BINDU has lower link traversal overhead

## Slide 31: Outline
Background: Deadlocks
Current Solutions
BINDU
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
  Deep Dive
Evaluations
  Methodology
  Results
Conclusion

## Slide 32: Revisiting Qualitative Comparison
Solution Proposed | Full Path Diversity | High Throughput | No Extra VCs | No Deadlock Detection | Topology agnostic
Dally’s Theory |  |  |  |  | 
Duato’s Theory |  |  |  |  | 
Flow Control |  |  |  |  | 
Recovery |  |  |  |  | 
Deflection |  |  |  |  | 
BBR |  |  |  |  | 
BINDU |  |  |  |  | 
*in all VCs except escape VC
*

## Slide 33: Conclusion
Deadlock is the problem which every network has to deal with
Current solutions either add turn restrictions (sacrificing path diversity), or require additional VCs, or require expensive circuitry to detect and recover from deadlocks
BINDU provides a novel way of resolving deadlock by providing one guaranteed empty VC in whole network that cycles through the network
BINDU provides performance benefits over both deadlock avoidance and deadlock recovery schemes at a low area/power overhead
BINDU enjoys full path-diversity, requires no additional VCs and is completely topology agnostic
Thank you!
BINDU
Questions?

## Slide 34: Mayank Parasar
mparasar3@gatech.edu
Thank you!