## Slide 1: SEESAW: Set Enhanced Superpage Aware caching
Mayank Parasar∑, Abhishek BhattacharjeeΩ, Tushar Krishna∑
∑School of Electrical and Computer Engineering
Georgia Institute of Technology
ΩDepartment of Computer Science
Rutgers University
mparasar3@gatech.edu
Set
Associativity
http://synergy.ece.gatech.edu/

## Slide 2: Outline
Motivation
SEESAW: Concept
SEESAW: Micro-architecture
Evaluation Methodology
Results
Conclusion

## Slide 3: L1 Cache Characteristics
Ideal-Cache
VIPT-Cache
Fast lookup
High hit-rate
Energy
Efficiency

## Slide 4: Virtually Indexed Physically Tagged [VIPT] Cache
TLB
PPN
Page Offset
tag
Data block
v
VPN
Page Offset
Set
index
block offset
Cache
HIT/MISS
VA
PA
Way-1
Way-2
Way-3
Way-4
Way-1
Way-2
Way-3
Way-4
set-1
set-N
Way-1
Way-2
Way-3
Way-4
Way-1
Way-2
Way-3
Way-4
=
VIPT Caches necessitate:
(set-index + block-offset) <= Page-offset

## Slide 5: Impact of Associativity on Access Latency and Energy of cache
Cache Access Latency
Cache Access Energy

## Slide 6: Effect of associativity on MPKI of cache
High Associativity hurts latency and energy without commensurately improving hit rate

## Slide 7: Revisiting L1 Cache Characteristics for VIPT Cache
Ideal-Cache
VIPT-Cache
Fast lookup
High hit-rate
Energy
Efficiency
Virtual
memory!
Virtual
memory!

## Slide 8: Opportunity: Superpage
Is it possible to relax constrains of
Traditional VIPT cache?
Yes
How ?
4-KB
2-MB
1-GB
More page-offset bits
for superpage!
HW and OS Support for Superpages in modern processors
Baseline Page
Super Page
Offset-bits:
12
Offset-bits:
21
Offset-bits:
30

## Slide 9: Prevalence of superpages in modern OSes under memory fragmentation
Ran on 32-core; Sandybridge; 32 GB RAM
Memhog causes memory fragmentation; higher %age indicates higher fragmentation

## Slide 10: Outline
Motivation
SEESAW: Concept
SEESAW: Micro-architecture
Evaluation Methodology
Results
Conclusion

## Slide 11: SEESAW: Concept
Less-sets
More-associativity
More-sets
Less-associativity
super-page
Base-page
tag
Data block
v
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-2
Way-2
Way-2
Way-2
Way-2
Way-2
Way-3
Way-3
Way-3
Way-3
Way-3
Way-3
Set:1
Set:2
Set:3
tag
Data block
v
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Way-1
Set:1
Set:3
Set:2
Set:4
Set:5
Set:6
Set:7
Set:8
Set:9
Faster
Energy-Efficient

## Slide 12: Outline
Motivation
SEESAW: Concept
SEESAW: Micro-architecture
Evaluation Methodology
Results
Conclusion

## Slide 13: SEESAW: Micro-architecture
VPN
Set index
block offset
Cache
VA
TLB
PPN
Basepage Offset
PA
set-N
set-1
tag
Data block
v
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Basepage Offset
tag
Data block
v
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
set-1
set-N
Partition bit
Translation Filter Table
(TFT)
Partition
decoder
Predicts whether page is superpage
Partition-0
Partition-1
Superpage offset
Decodes partition index from partition bit

## Slide 14: SEESAW: Micro-architecture
VPN
Set index
block offset
VA
TLB
PPN
Basepage Offset
PA
set-N
set-1
tag
Data block
v
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Basepage Offset
tag
Data block
v
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
set-1
set-N
Partition bit
Translation Filter Table
(TFT)
Partition
decoder
Partition-0
Partition-1
Cache
Superpage offset

## Slide 15: SEESAW: Superpage access
VPN
Set index
block offset
VA
TLB
PPN
Basepage Offset
PA
set-N
set-1
tag
Data block
v
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Basepage Offset
tag
Data block
v
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
set-1
set-N
Partition bit
Translation Filter Table
(TFT)
Partition
decoder
Partition-0
Partition-1
Cache
Super Page
Superpage offset
=
HIT/MISS

## Slide 16: SEESAW: Basepage access
VPN
Set index
block offset
VA
TLB
PPN
Basepage Offset
PA
set-N
set-1
tag
Data block
v
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Basepage Offset
tag
Data block
v
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
set-1
set-N
Partition index
Translation Filter Table
(TFT)
Partition
decoder
Partition-0
Partition-1
Cache
Not a Super Page
=
HIT/MISS

## Slide 17: SEESAW: TFT and Partition Decoder
Super
page?
Tag: VA[63:21]
Partition
decoder
Translation Filter Table
(TFT)
Translation Filter Table
  TFT Lookup
    Direct mapped
    False negative due to size
  TFT Update
    VA misprediction
    2MB L1-TLB fill
    2MB L1-TLB Invalidation
Partition Decoder
  For 32kB Cache
  For 64kB Cache

## Slide 18: SEESAW: Cache line insertion policy
VPN
Set index
block offset
VA
TLB
PPN
Baseline Page Offset
PA
set-N
set-1
tag
Data block
v
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Way-3
Way-4
Baseline Page Offset
tag
Data block
v
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
Way-1
Way-2
set-1
set-N
Partition bit
Translation Filter Table
(TFT)
Partition
decoder
Partition-0
Partition-1
Cache
Which partition should cache-line be inserted?

## Slide 19: SEESAW: Cache line insertion policy
4way-8way
  Superpage miss: victim within the partition
  Basepage miss: victim within the set
4way
  Uses LRU within the associated partition
  Avoid installing the same line twice
  Saves energy

## Slide 20: SEESAW: System Level Optimization
Cache coherence
  Cache coherence lookups use physical address
  Snoopy provide higher energy benefits over Directory based coherence
Page table modifications
  Superpage splintered into multiple basepages
  Multiple basepages promoted to superpages

## Slide 21: Outline
Motivation
SEESAW: Concept
SEESAW: Micro-architecture
Evaluation Methodology
Results
Conclusion

## Slide 22: SEESAW: Simulated system

## Slide 23: SEESAW: Workloads
Spec
Parsec
Cloudsuite
  Tunkrank
Biobench
  Mummer
  Tiger
MongoDB
Server Workload
  graph500
  Nutch Hadoop
Social-event web service
  Olia
Key value store
  Redis

## Slide 24: Outline
Motivation
SEESAW: Concept
SEESAW: Micro-architecture
Evaluation Methodology
Results
Conclusion

## Slide 25: SEESAW: Performance improvement
SEESAW observes 3-10% better runtime over baseline

## Slide 26: SEESAW: Performance improvement
Out-of-order
CPU
in-order
CPU
~10% performance improvement for 64kB cache in OoO CPUs

## Slide 27: SEESAW: Energy savings
10-20% more energy savings over CPUs using baseline VIPT caches!
Approx. one-third of energy savings from coherence

## Slide 28: SEESAW: TFT analysis and Way-Prediction
TFT Analysis
SEESAW + Way-prediction
16-entry TFT drives miss-rate under 10%
SEESAW+WP shows symbiotic behavior

## Slide 29: Outline
Motivation
SEESAW: Concept
SEESAW: Micro-architecture
Evaluation Methodology
Results
Conclusion

## Slide 30: Revisiting L1 Cache Characteristic
Ideal-Cache
VIPT-Cache
Fast lookup
High hit-rate
Energy
Efficiency
SEESAW
Cache

## Slide 31: SEESAW: Conclusion
Set
Associativity
L1 caches are optimized for latency
  VIPT imposes indirect restriction on number of sets in a L1 cache, increasing associativity
  There is non-linear relation between associativity and access latency/energy of the L1 cache
Superpages are often used in modern OSes
  SEESAW provides low-associative access to superpages, providing both latency and energy benefits
  Up to 10 % performance improvement and 20 % energy reduction in modern workloads
SEESAW has extremely low-overhead and is readily implementable
Thank you!